Dawn Mission to Vesta and Ceres

L-0 Data from Ceres

Gravity Science Instrument

Archive Volume Software Interface Specification

Dustin Buccino

Jet Propulsion Laboratory, California Institute of Technology

Version 3.1

February 26, 2019

(c) 2019 California Institute of Technology. Government sponsorship acknowledged.

CHANGE LOG

| DATE | CHANGES | REASON | REVISION |
| --- | --- | --- | --- |
| 06/29/15 | Updated from Vesta to Ceres |  | 2.0 |
| 03/02/16 | Added references for multiple PDS deliveries for Ceres |  | 2.1 |
| 02/24/17 | Updated for final delivery |  | 2.2 |
| 05/30/17 | Updated for peer review |  | 2.3 |
| 01/11/19 | Updated for re-release (version 2.0) of Ceres raw dataset | XM2 data archival | 3.0 |
| 02/26/19 | Updated for peer review of XM2 data |  | 3.1 |

TABLE OF CONTENTS

1.	INTRODUCTION	4

1.1.	Purpose and Scope	4

1.2.	Data Overview	4

1.3.	Content Overview	5

1.4.	References	5

2.	RAW DATA ARCHIVE OVERVIEW	5

2.1.	Instrument Overview	5

2.2.	Data Product Overview	6

2.2.1.	Detailed Descriptions	6

2.3.	Data Processing	9

2.4.	Software	9

2.5.	File Naming Conventions	9

2.6.	Data Product Labels	9

2.7.	Standard Keyword Values	9

3.	ARCHIVE ORGANIZATION	10

3.1.	Root Directory	10

3.2.	ANCILLARY Directory	10

3.3.	CATALOG Directory	11

3.4.	DOCUMENT Directory	11

3.5.	INDEX Directory	11

3.6.	ODF Directory	11

3.1.	TNF Directory	12

4.	RELEVANT DATA ARCHIVED AT OTHER SITES	12

4.1.	NAIF Node	12

4.2.	Optical Navigation Data – Small Bodies Node	12

5.	PERSONNEL	12

6.	ACKNOWLEDGEMENTS	13

7.	APPENDIX	13

7.1.	Spacecraft Antenna Locations	13

7.2.	Deep Space Network Antenna Locations	13

ACRONYMS AND ABBREVIATIONS

ASCII		American Standard Code for Information Interchange

CEGR		Ceres Gravity

CK		C-Kernel

DOM		Distributed Object Manager

DOY		Day of Year

DSC		Dawn Science Center

DSN		Deep Space Network

GS		Gravity Science

GSI		Gravity Science Instrument

HGA		High Gain Antenna

ION		Ionosphere (in reference to Ionosphere calibration files)

JPL		Jet Propulsion Laboratory

LGA		Low Gain Antenna

NAIF		Navigation Ancillary Information facility

NASA		National Aeronautics and Space Administration

ODF		Orbit Data File

PDS		Planetary Data System

RDA		Raw Data Archive

RS		Radio Science

RSS		Radio Science Subsystem

RSSG		Radio Science Systems Group

SCLK		Spacecraft Clock Kernel

SIS		Software Interface Specification

SFF		Small Forces File

SNR		Signal-to-Noise Ratio

TNF		Tracking and Navigation Service Data Files

TRO		Troposphere (in reference to Troposphere calibration files)

TSAC		Tracking System Analytic Calibration

VEGR		Vesta Gravity

WEA		Weather (in reference to DSN Weather files)

# INTRODUCTION

## Purpose and Scope

This Software Interface Specification (SIS) describes the format and content of the Dawn Mission to Vesta and Ceres (Dawn) Gravity Science (GS) Raw Data Archive (RDA) for the Ceres phase of the mission. The Dawn Ceres Gravity (CEGR) RDA represents the complete archive of raw data from gravity science investigations conducted using the radio link between the Dawn spacecraft and the Deep Space Network (DSN) tracking stations. The archive is generated by the Dawn Gravity Science Team and the Dawn Science Center (DSC). It is maintained and distributed by the Planetary Data System (PDS).

Gravity Science is a subset of Radio Science, and because of this, the terms Gravity Science (GS) and Radio Science (RS) are used interchangeably in this archive; as are the terms the Gravity Science Instrument (GSI) and Radio Science Subsystem (RSS).

## Data Overview

This data set contains archival raw, partially processed, and ancillary/supporting gravity science data acquired during the Dawn mission while the spacecraft was in orbit around the asteroid Ceres. The radio observations were carried out using the Dawn spacecraft and Earth-based receiving stations of the NASA Deep Space Network. The data set was designed primarily to support generation of high-resolution gravity field models for Ceres. Of most interest are likely to be the Orbit Data Files in the ODF directory and Tracking and  Navigation Files in the TNF directory, which provided the raw input to gravity investigations, as well as the ionospheric and tropospheric media calibration files in the ION and TRO directories, respectively.

The closed-loop system of the Deep Space Network used a phase-lock loop in the ground receiver to track the downlink signal from the Dawn spacecraft, reporting both amplitude and frequency at rates typically of 1-10 times per second. Closed-loop data are efficient for characterizing slowly changing signals and are the input to operational navigation and orbit-determination processes.

The data set includes two types of primary data, the TNF and the ODF. TNFs (Tracking and Navigation Service Data Files) are the output of the closed-loop receiver. Orbit Data Files (ODFs) are compressed versions of TNFs. ODFs are specifically targeted to spacecraft navigators and scientists interested in gravity fields.

In September 2017, the Deep Space Network retired the TRK-2-18 ODF file format. It is replaced by only the TRK-2-34 TNF files. Before September 2017, all tracking data is stored in ODF format files. After September 2017, all tracking data is stored in TNF format files.

Typical users of these data might analyze range and Doppler measurements in ODFs to reconstruct the spacecraft trajectory.  Relevant questions would include the measurement uncertainties in range and Doppler at different DSN antennas (typical Doppler uncertainty at 10 second integration time is 50 microns/sec, for further details see INST.CAT); the uncertainties could set constraints on any model of Ceres's gravity field developed later, for example.

## Content Overview

This SIS describes the format and content of the Dawn GS RDA. There is minimal processing done of the data collected. This archive is delivered to the PDS via the DSC by the Gravity Science Team. The DSC delivers the completed archives to PDS with the DATA_SET_ID of DAWN-A-RSS-CEGR-V2.0.

Version 2.0 of this dataset adds the raw and ancillary/supporting radio science data from Dawn during the Extended Mission 2 (XM2) mission phase around Ceres. Gravity observations in the XM2 phase began on June 6, 2018. There were no gravity observations between the end of the prime mission in September 2017 and the start of XM2 in June 2018.

The following data are archived:

- ODF: Orbit Data Files; contain the minimally processed output of the closed-loop receiver, including Doppler

- TNF: Tracking and Navigation Files; contain the most verbose output of the closed-loop receiver, including Doppler and phase (available for XM2 phase only)

- APC: Antenna Phase Center file; contains the times when the phase center changes due to selection of a low gain antenna (default is the high gain antenna)

- ION: Ionosphere calibration files; contains historical and predicted Earth ionosphere conditions

- SCM: Spacecraft mass report file; contain the spacecraft mass, center of mass, and propellant usage over time

- SFF: Small forces files; contain spacecraft thruster firing data

- TRO: Troposphere calibration files; contain historical and predicted Earth troposphere conditions

- WEA: DSN weather files; contain the weather conditions at each tracking station

## References

- Deep Space Network Telecommunications Link Design Handbook, JPL-E-810-005, Jet Propulsion Laboratory, Pasadena, CA, 2013.

- Park R.S., A.S. Konopliv, B.G. Bills, N. Rambaux, J.C. Castillo-Rogez, C.A. Raymond, A.T. Vaughan, A.I. Ermakov, M.T. Zuber, R.R. Fu, M.J. Toplis, C.T. Russell, A. Nathues and F. Preusker, A partially differentiated interior for (1) Ceres deduced from its gravity field and shape, Nature 537, 515-517, doi:10.1038/nature18955, 2016.

# RAW DATA ARCHIVE OVERVIEW

## Instrument Overview

The gravity science instrument utilizes the deep space transponder onboard the Dawn spacecraft and Doppler tracking equipment at the Deep Space Network to perform radio science investigations to determine the gravitational field of celestial bodies.

For the full description of the Gravity Science instrument, please refer to the INST.CAT and DATASET.CAT files in the CATALOG directory.

## Data Product Overview

The ODFs and TNFs are binary files with detached PDS labels. The ancillary data products (APC, ION, SCM, SFF, TRO, and WEA) are ASCII files. The table below describes the data products contained in these directories.

| File | Abbrev. | File Type | Average File Size | Generation Frequency | Source of Files |
| --- | --- | --- | --- | --- | --- |
| Orbit Data File | ODF | Binary | 100K | Per request | DSN/OSCARX |
| Tracking and Navigation File | TNF | Binary | 20M | Once per pass | DSN/OSCARX |
| Antenna Phase Center files | APC | ASCII | 4K | Once | Dawn Gravity Team |
| Ionosphere Calibration files | ION | ASCII | 24K | Monthly | TSAC/OSCARX |
| Spacecraft Mass Report | SCM | ASCII | 8K | Per request | Dawn DOM |
| Small Forces Files | SFF | ASCII | 2.5M | Per mission phase | Dawn DOM |
| Troposphere Calibration files | TRO | ASCII | 150K | Monthly | TSAC/OSCARX |
| DSN Weather files | WEA | ASCII | 1.1M | Weekly | TSAC/OSCARX |

### Detailed Descriptions

Unless otherwise noted, the abbreviations ‘yyyy’ indicate the year, and ‘ddd’ indicate the day of year. In a series, such as ‘yyyy_ddd_yyyy_ddd’, the first date (‘yyyy_ddd’) indicates the starting date and the second date indicates the end date that the file is applicable for. If only one sequence of dates is provided, it is the applicable start time of the file.

Orbit Data File

The ODF is a minimally processed output of the closed-loop receiver. It contains the most important information (range, Doppler and frequency ramps) needed by spacecraft investigators, and investigators interested in determining gravity fields. Each ODF is accompanied by a full PDS label which describes both the content and format of the associated file. ODF data fields include:

- Narrowband spacecraft VLBI, Doppler mode (cycles)

- Narrowband spacecraft VLBI, phase mode (cycles)

- Narrowband quasar VLBI, Doppler mode (cycles)

- Narrowband quasar VLBI, phase mode (cycles)

- Wideband spacecraft VLBI (nanoseconds)

- Wideband quasar VLBI (nanoseconds)

- One-way Doppler (Hertz)

- Two-way Doppler (Hertz)

- Three-way Doppler (Hertz)

- One-way total count phase (cycles)

- Two-way total count phase (cycles)

- Three-way total count phase (cycles)

- PRA planetary operational discrete spectrum range (range units)

- SRA planetary operational discrete spectrum range (range units)

- RE(GSTDN) range (nanoseconds)

- Azimuth angle (degrees)

- Elevation angle (degrees)

- Hour angle (degrees)

- Declination angle (degrees)

ODFs are abstracted from subsets of TNF data, the uncompressed output of the closed-loop receiver at the Deep Space Network.  A full PDS label accompanies each ODF file and gives a bit level description of the content and format.

ODFs are stored in the ODF directory. ODFs contain the output of the closed-loop tracking system of the Deep Space Network. File names are of the form DAWNCEGRyyyy_ddd_hhmmXuuwVn.ODF where 'DAWNCEGR' identifies the mission and the data set; 'yyyy' is the four-digit year, 'ddd' is the three-digit day-of-year, 'hh' is the two-digit hour, and 'mm' is the two-digit minute at the beginning of the file; 'X' indicates an X-Band uplink ('N' denotes no uplink); 'uu' indicates the uplink station (set to 'NN' for no uplink or 'MM' for two or more uplinking stations during the time interval covered), 'w' indicates the downlink mode ('1', '2', '3', or 'M' for 1-way, 2-way, 3-way, or 'multiple', respectively), and 'Vn' indicates the version number of the file.  The ODF label has file name DAWNCEGRyyyy_ddd_hhmmXuuwVn.LBL. The typical ODF contains about 100 Kbytes.

Tracking and Navigation File

In September 2017, the Deep Space Network retired the TRK-2-18 ODF file format. It is replaced by only the TRK-2-34 TNF files. Before September 2017, all tracking data is stored in ODF format files. After September 2017, all tracking data is stored in TNF format files.

TNFs contain the most primitive (and most voluminous) output from the closed-loop radio science system; they are stored in the TNF directory. File names are of the form DAWNCEGRyyyy_ddd_hhmmXuuwVn.TNF where 'DAWNCEGR’ identifies the mission and the data set; 'yyyy' is the four-digit year, 'ddd' is the three-digit day-of-year, 'hh' is the two-digit hour, and 'mm' is the two-digit minute at the beginning of the file; 'X' indicates an X-Band uplink ('N' denotes no uplink); 'uu' indicates the uplink station (set to 'NN' for no uplink or 'MM' for two or more uplinking stations during the time interval covered), 'w' indicates the downlink mode ('1', '2', '3', or 'M' for 1-way, 2-way, 3-way, or 'multiple', respectively), and 'Vn' indicates the version number of the file.  Dates and times in the file name are UTC. The TNF label has file name DAWNCEGRyyyy_ddd_hhmmXuuwVn.LBL. The typical TNF contains about 20 Mbytes.

Unlike the ODF files, the TNF files do not have a complete data label but rather a minimal label. This is due to the complicated nature of the data format. The format of these TNF data are described in detail in the TNFSIS.LBL document in the DOCUMENT directory.

Antenna Phase Center files

Antenna Phase Center files were produced by the JPL Dawn Gravity Science Team. The Dawn spacecraft utilizes four antennas during operations (1 high gain antenna and 3 low gain antennas). The Antenna Phase Center files contain the start times and stop times when any of the low gain antennas were being used. During times not specified in these files, the high gain antenna was being used. The original sources of these data are the Dawn Sequence of Events (SOE) files. APC files are ASCII files. File names have the form DAWNCEGR_yyyy_ddd_yyyy_ddd.APC. The accompanying PDS label (with name DAWNCEGR_yyyy_ddd_yyyy_ddd.LBL) describes the content and structure of the file.

Ionosphere Calibration files

Ionosphere Calibration files are ASCII files produced by the Tracking System Analytic Calibration (TSAC) Group at JPL. They provide historical and predicted Earth ionospheric conditions. File names have the form DAWNCEGR_yyyy_ddd_yyyy_ddd.ION. Each ION file is accompanied by a PDS minimal label with file name DAWNCEGR_yyyy_ddd_yyyy_ddd.LBL. Typical file size is 24 KB. Format and content of the files are described by TRK_2-23_REVC_L5 in the DOCUMENT directory.

Spacecraft Mass Report

Spacecraft Mass History files were produced by the Dawn Spacecraft Team. They contain the estimates of the spacecraft mass, center of mass, and propellant usage. These are ASCII files of variable length records. File names have the form DAWNCEGR_yyyy_ddd.SCM, where

yyyy_ddd is the applicable start time of the file. Files are accompanied by a PDS label describing the format of the data. Typical file size is 8 KB. The accompanying PDS label describes the content and structure of the file.

Small Forces Files

Small Forces Files were created from the Dawn spacecraft engineering telemetry stream. These are ASCII files of variable length records.  File names have the form DAWNCEGR_yyyy_ddd_yyyy_ddd.SFF.  Each SFF file is accompanied by a PDS minimal label with file name DAWNCEGR_yyyy_ddd_yyyy_ddd.LBL. Typical file sizes are 2.5 MB. File content and structure are defined by NAV018-SFF-JPL.DOC in the DOCUMENT directory.

Troposphere Calibration files

Troposphere Calibration files are ASCII files produced monthly by the Tracking System Analytic Calibration (TSAC) Group at JPL. They provide historical and predicted Earth tropospheric conditions. File names have the form DAWNCEGR_yyyy_ddd_yyyy_ddd.TRO. Each TRO file is accompanied by a PDS minimal label with file name DAWNCEGR_yyyy_ddd_yyyy_ddd.LBL. Typical file size is 150 KB. Format and content of the files are described by TRK_2-23_REVC_L5 in the DOCUMENT directory.

DSN Weather files

DSN Weather files were produced by the Tracking System Analytic Calibration (TSAC) Group at JPL. Files give weather calibration information for DSN complexes. These are ASCII files of variable length records.  File names have the form DAWNCEGR_yyyy_ddd_yyyy_ddd_ss.WEA, where 'ss' is the DSN complex where weather data were acquired. WEA files are typically released weekly and contain all weather data for the complex since 1 January. Only files covering the entire years of 2011 and 2012 are included in the archive. Each WEA file is accompanied by a PDS minimal label with file name DAWNCEGR_yyyy_ddd_yyyy_ddd_ss.LBL.

The files grow at the rate of approximately 90 KB per month. Format and content of the files are described by T2_24_L5 in the DOCUMENT directory.

## Data Processing

Data processing is performed by various groups and organizations at the Jet Propulsion Lab and the Deep Space Network. For details on each individual type, refer to the appropriate document in the DOCUMENT directory of this archive.

## Software

No software is included in this archive. The SPICE toolkit provides useful tools and algorithms for data processing of this type and is located at the NAIF PDS node naif.jpl.nasa.gov.

## File Naming Conventions

See Section 2.2.1 for file naming conventions in the description of each file type.

## Data Product Labels

Every file in this archive is accompanied by a PDS label. The label is either attached (embedded in the file) or detached (separate file with same name except for extension ‘.LBL’). All data files in the ANCILLARY and ODF directory have detached PDS labels. Depending on the file type, the detached label may provide the content and structure of the file. Labels are structured in the PDS KEYWORD=VALUE fashion. A description of the keywords may be found on the web at http://pds.nasa.gov/tools/ddlookup/data_dictionary_lookup.cfm.

## Standard Keyword Values

The Dawn Gravity Science RDA uses the following standard keywords and values, consistent across the archive:

| Keyword | Dawn Standard Values |
| --- | --- |
| DATA_SET_ID | DAWN-A-RSS-1-CEGR-V2.0 |
| DATA_SET_NAME | “DAWN CERES RAW GRAVITY SCIENCE V2.0” |
| INSTRUMENT_HOST_ID | DAWN |
| INSTRUMENT_HOST_NAME | DAWN |
| INSTRUMENT_ID | RSS |
| INSTRUMENT_NAME | GRAVITY SCIENCE INSTRUMENT |
| INSTRUMENT_TYPE | RADIO SCIENCE |
| MISSION_NAME | DAWN MISSION TO VESTA AND CERES |
| TARGET_NAME | 1 CERES, 4 VESTA |
| VOLUME_ID | DWNCGRS_0 |
| VOLUME_SERIES_NAME | DAWN |
| VOLUME_SET_ID | USA_NASA_PDS_DWNCGRS_0 |
| VOLUME_SET_NAME | “DAWN MISSION TO CERES RAW GRAVITY OBSERVATIONS” |
| VOLUME_VERSION_ID | VERSION 2 |

# ARCHIVE ORGANIZATION

The Dawn Gravity Science Raw Data Archive for Ceres has the following directories:

- Root directory

  - ANCILLARY

    - APC

    - ION

    - SCM

    - SFF

    - TRO

    - WEA

  - CATALOG

  - DOCUMENT

  - INDEX

  - ODF

  - TNF

The contents of the directories are described below.

## Root Directory

This directory is the core directory on which the rest of the archive is built. It contains the following files:

- AAREADME.TXT: Human readable description of the archive contents

- ERRATA.TXT: Human readable list of corrections and other comments regarding the archive

- VOLDESC.CAT: Description of the contents of the volume

## ANCILLARY Directory

The ANCILLARY directory contains data that are useful in the analysis of the primary data, the ODF files. It contains the following subdirectories and file types:

| Directory | File Type | Contents |
| --- | --- | --- |
| APC | Antenna Phase Center | Antenna phase center times and PDS label |
| ION | Ionosphere Calibration | Ionosphere calibration files and PDS labels |
| SCM | Spacecraft Mass Report | Spacecraft mass history and PDS labels |
| SFF | Small Forces Files | Small forces files and PDS labels |
| TRO | Troposphere Calibration | Troposphere calibration files and PDS labels |
| WEA | DSN Weather files | Weather records from the DSN and PDS labels |

## CATALOG Directory

This directory contains descriptions of the dataset, mission, instrument, and spacecraft. They are all ASCII stream files. It contains the following files:

- CATINFO.TXT: Description of the directory

- DATASET.CAT: Overview of the RDA

- INST.CAT: Overview of the Gravity Science Instrument

- DAWNINSTHOST.CAT: Overview of the Dawn spacecraft

- DAWNMISSION.CAT: Overview of the Dawn Mission to Vesta and Ceres

- PERSON.CAT: Contributors to the archive and contact information

- REF.CAT: References for the archive

## DOCUMENT Directory

This directory contains the corresponding documentation to help the end user use and interpret the data included in this archive. The following documents are included:

| Filename | Format | Description |
| --- | --- | --- |
| DOCINFO.TXT | text | Description of the directory |
| Dawn_Ceres_Grav_SIS | Word, PDF, HTML | This document |
| T2-18-L5 | HTML, PDF | Description of the Orbit Data Files (ODF) and binary format |
| TRK-2-23-RevC-L5 | HTML, PDF | Description of the DSN Media Calibration files (ION, TRO) |
| T2-24-L5 | HTML, PDF | Description of the DSN Weather files (WEA) |
| DAWN_SFF_SIS | HTML, PDF | Description of the Small Forces Files (SFF) |
| TNFSIS | text, PDF | Description of the Tracking and Navigation Files (TNF) and binary format |

## INDEX Directory

This directory contains the following files:

- INDEXINFO.TXT: Description of the directory

- INDEX.LBL: Detached label describing INDEX.TAB

- INDEX.TAB: Table listing all data products in the RDA

## ODF Directory

The ODF directory contains the binary Orbit Data Files, one of the primary data types, for the Dawn Ceres Gravity Science RDA. Each is accompanied by a detached PDS label describing the format of the ODF file. For more details, see Section 2.2.1 of this document.

## TNF Directory

The TNF directory contains the binary Tracking and Navigation Files, one of the primary data types, for the Dawn Ceres Gravity Science RDA. Each is accompanied by a minimal detached PDS label. For more details, see Section 2.2.1 of this document.

# RELEVANT DATA ARCHIVED AT OTHER SITES

## NAIF Node

The Navigation and Ancillary Information Facility (NAIF) is the navigation node of the PDS. NAIF provides the archives for spacecraft navigation, attitude, events, clock conversion, and planetary ephemerides for most NASA missions. Additionally, NAIF provides the SPICE toolkit, containing useful algorithms to utilize and manipulate data NAIF provide.

Relevant to gravity science are the following types:

- CK: Spacecraft and solar array attitude orientation files

- EK: Spacecraft events kernel

- FK: Reference frame specification

- SCLK: Conversion between spacecraft time and ephemeris time

- SPK: Spacecraft and Planetary ephemeris data

The NAIF PDS archive for Dawn is located at:

- naif.jpl.nasa.gov/pub/naif/pds/data/dawn-m_a-spice-6-v1.0/

## Optical Navigation Data – Small Bodies Node

The PDS Small Bodies Node (SBN), the location of this archive, also hosts the data from the Dawn Framing Camera 2 (FC2) instrument. The Dawn FC2 archives include the optical navigation data, which aids the analysis of the DSN radiometric tracking data contained in this archive.

The PDS Small Bodies Node is located at:

- sbn.psi.edu/

The Framing Camera 2 imaging data may be easily located via the following URL:

- https://sbn.psi.edu/pds/resource/dwncfc2.html

# PERSONNEL

- Ryan S. Park, Chair of the Dawn Gravity Science Working Group, NASA Jet Propulsion Lab

- Alexander  S. Konopliv, Dawn Gravity Science Co-Investigator, NASA Jet Propulsion Lab

- Sami W. Asmar, Dawn Gravity Science Co-Investigator, NASA Jet Propulsion Lab

- Andrew T. Vaughan, Dawn Gravity Science Analyst, NASA Jet Propulsion Lab

- Dustin R. Buccino, Dawn Radio Science Analyst, NASA Jet Propulsion Lab

# ACKNOWLEDGEMENTS

The work was carried out at the Jet Propulsion Laboratory, California Institute of Technology, under a contract with the National Aeronautics and Space Administration.

# APPENDIX

## Spacecraft Antenna Locations

The Dawn spacecraft has four antennas onboard the spacecraft. In the spacecraft-fixed frame, the phase centers are:

| Body ID | X-component (meters) | Y-component (meters) | Z-component (meters) |
| --- | --- | --- | --- |
| PLUS_X_HGA | 1.22 | 0.00 | 1.58 |
| PLUS_X_LGA | 0.99 | 0.45 | 0.33 |
| PLUS_Z_LGA | 0.26 | -0.43 | 2.29 |
| MINUS_Z_LGA | 0.45 | 0.45 | -0.01 |

## Deep Space Network Antenna Locations

The Deep Space Network has multiple antennas at three sites in Goldstone, California, United States; Canberra, Australia; and Madrid, Spain. Station locations are documented in [DSN810-5] (see references in CATALOG/REF.CAT). The locations are also available in CATALOG/INST.CAT.